## Slide 1
The ALIX line — ERMASMART (ERM Automatismes) · CR5 cobot under AR
INTERNSHIP · EULER LABORATORY · ISAE-SUPMÉCA
Mechatronics Modelling
of an Entire Industry 5.0
Production Line
Intern: Ms. Samiksha Satre
Duration: 4 Months
Supervisor: Mr.Romain Delabeye
Co-supervisor: Dr.Shriniwas Metan
Period: February 2026 To June 2026
Location: Isae-supméca Paris, France
Electronics & Telecommunication Engineering department
N. K. Orchid College of Engineering & Technology, Solapur

## Slide 2
AGENDA
Euler Laboratory
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
2
THE MISSION
THE SYSTEM
STATIONS
SPATIAL & COUPLING ANALYSIS
DELIVERABLES
CONCLUSION
MODEL CALLIBRATION
THE HEADLINE-PERFORMANCE METRICS
REAL-TIME EXPERIMENT ON THE ALIX LINE
MULTIPHYSICS MODELS,EQUATIONS
ENERGY ANALYSIS
PER-SUBSYSTEM VALIDATION RESULTS AND TWO STAGE VALIDATION

## Slide 3
THE MISSION
From physical line to digital twin
The objective: build a unified process, mechatronic and multiphysics model of an entire Industry 5.0 production line.
1
Analyse the line architecture & mechatronic subsystems
2
Model each subsystem in Modelica (mech · electrical · thermal)
3
Integrate the production sequence & process logic
4
Export to FMUs and orchestrate from Python via FMI
5
Simulate the whole line end-to-end from one program
6
Identify parameters & validate against measurements
Euler Laboratory
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-SupmécaSSSS
3

## Slide 4
THE SYSTEM
ALIX — the ERMASMART Industry 5.0 line
ALIX is the lab's ERMASMART line by ERM Automatismes (Carpentras, France) — a bench-top flexible line showcasing smart sensors, IO-Link, supervision, cobotics, vision & RFID traceability.
8445 mm
line length
3-ph
244 V phase · 50 Hz
S7-1200
Siemens PLC · TULIP
30 s
finished pot
The five stations
ON10
Bin-picking cobot
2D vision feed-in
›
DX10
Dosing axis
fills pots
›
CR5
Capping cobot
6-DOF Dobot
›
XY10
Cartesian XYZ
packs into trays
›
VL10
Vertical magazine
finished-tray store
Continuous conveyor belt — runs through all five stations
Coloured = modelled in this project
4
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca

## Slide 5
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
5
VISUAL REPRESENTATION OF ALIX LINE

## Slide 6
THE MODELS
Three subsystems · three physics domains
CONVEYOR
Full multiphysics
Electrical → mechanical → thermal
3-phase induction machine
TECHTOP 0.09 kW · NMRV gearbox i = 20
Thermal branch: losses → ambient
15 Modelica blocks · 161 parameters
CR5 COBOT
6-DOF multibody
Dobot CR5 — 6 revolute joints
Geometry from real CAD
Mass / COM / inertia per link
6 torque inputs · 16 outputs
The actual robot, not a generic arm
XY10 STATION
Cartesian + vacuum
3 axes (X·Y·Z) closed-loop
PID → DC drive → lead-screw → stage
Vacuum gripper (Boolean force)
DC-equivalent of chopper drive
4 inputs · 11 outputs
The conveyor runs continuously; CR5 and XY10 act in discrete bursts — the model captures both regimes.
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
6

## Slide 7
MULTIPHYSICS MODEL 1 · CONVEYOR
Electrical → mechanical → thermal chain
3-ph supply
244 V · 50 Hz
→
Induction
motor
→
Gearbox
i = 20
→
Drum +
belt load
Key parameters
Stator / rotor R | 12 Ω / 8 Ω
Magnetising Lm | 0.45 H
Leakage Lσ | 0.025 H
Pole pairs | 2 (4-pole)
Gear ratio | 20
Heat capacity C | 500 J/K
Conductance G / τ | 1.5 W/K · 333 s
Steady-state prediction: 1499 rpm 1.629 A RMS 107.96 W
Thermal FMU — verified vs analytical
+11.95 K motor-body rise in 60 s model vs analytical agreement 99.2%. P_elec matches the 3DEXPERIENCE reference to 0.0003 W.
6
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca

## Slide 8
1.Conveyor Motor Model
7
Architecture diagram
Electrical
───────────────
3-phase 244 V
50 Hz supply
Mechanical
───────────────
Motor shaft
torque + ω
Thermal
───────────────
Body heat
capacity C
Stator + rotor
(squirrel cage)
Air-gap torque
equation
Conductance G
to ambient
Copper + iron losses
(heatPort)
Ambient 20 °C
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca

## Slide 9
CONVEYOR (mechanical + thermal) EQUATIONS
Induction
motor
Gearbox
i = 20
6
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
MECHANICAL (rotational then translational)
Motor rotational dynamics:
Gearbox (ideal, ratio i_gear = 20):
Drum-to-belt conversion (r_drum = 25 mm):
Belt mass dynamics:
THERMAL (lumped 1st-order, motor housing)
Power losses:
Thermal time constant:
-> motor takes ~16 min (5*tau) to reach steady-state
Steady-state temperature rise:
For P_loss = 18 W: delta_T_ss = 12 K -> validated (11.86 K measured)
8

## Slide 10
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
9
Fig No.1.Conveyor motor model
CONVEYOR MOTOR MODEL

## Slide 11
10
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
Fig No.2.Conveyor motor model FMU Verification
CONVEYOR FMU VALIDATION

## Slide 12
MODEL 2 · CR5 COBOT
A faithful 6-DOF multibody twin
Kinematic chain (Dobot CR5 axis convention)
J1
axis Z
—
J2
axis Y
—
J3
axis Y
—
J4
axis X
—
J5
axis Y
—
J6
axis Z
Geometry from the real robot
Per-link mass, COM and inertia extracted from the public CR5 CAD in 3DEXPERINCE; 6× Revolute + 6× BodyShape, Newton-Euler assembled automatically by the MultiBody library.
94.9%
Mass agreement
model 23.74 kg vs brochure 25 kg
Joint-2 gravity pendulum period matches
CR5 Model
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
11

## Slide 13
CR5 COBOT MODEL PHYSICS
KINEMATIC CHAIN
World -> J1(Z) -> L1 -> J2(Y) -> L2 -> J3(Y) -> L3
-> J4(X) -> L4
-> J5(Y) -> L5
-> J6(Z) -> L6 -> TCP
EQUATION OF MOTION (Newton-Euler, manipulator form)
M(q) * q_ddot + C(q,q_dot)*q_dot + g(q) = tau - D * q_dot
where:
q in R^6 = joint angles
M(q) = 6x6 inertia matrix (configuration-dependent)
C(q,q_dot) = Coriolis/centripetal matrix
g(q) = gravity vector
tau = 6x1 applied joint torques (FMU inputs)
Inertia tensor at CoM:
I_xx = I_yy = (1/12)*m*(3*r^2 + L^2)
I_zz = (1/2)*m*r^2
VALIDATION
Total mass: 23.74 kg
Brochure spec: 25.00 kg
Agreement: 94.9 % -> 1.26 kg gap = cable harness + flange
12

## Slide 14
Fig No.3. CR5 COBOT model
13
CR5 COBOT MODEL

## Slide 15
14

## Slide 16
MODEL 3 · XY10 STATION
Cartesian gantry + vacuum gripper
Closed-loop drive (per axis · ×3 for X · Y · Z)
Position
command
›
PID
›
DC-equiv
voltage
›
R-L
winding
›
DC
machine
›
Lead-screw
(rot→lin)
›
Linear
stage
Position feedback closes the loop · vacuum gripper: Boolean command → switch → grip force
Honest abstraction: DC-equivalent steppers
Real steppers fire ±20 A in chopper mode; the FMU models a smooth ±3 A time-averaged drive. At line-orchestration level what matters is envelope, timing and energy all captured. Chopper detail belongs to EMC studies, not digital-twin operation. A documented engineering choice, not an omission.
XY10 Station
15

## Slide 17
MODEL 3 · XY10 STATION PHYSICS
CONTROL (PD position loop)
ELECTRICAL (DC-equivalent of stepper)
Back-EMF term K_t*(2*pi/lead)*dx/dt converts linear velocity into induced voltage opposing motion.
FORCE TRANSMISSION (lead-screw, lossless ideal)
MECHANICAL (Newton + friction + end-stops)
PNEUMATIC (1st-order Venturi vacuum)
PARAMETERS
16

## Slide 18
17
XY10 STATION MODEL

## Slide 19
18
XY10 STATION FMU VALIDATION

## Slide 20
SPATIAL LAYOUT & COUPLING ANALYSIS
4
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
19

## Slide 21
FIVE COUPLING PATHWAYS IDENTIFIED
ELECTRICAL - Shared 400 V three-phase bus
Captured: ideal source per subsystem
Phase 2: shared impedance bus
PNEUMATIC - Shared 5 bar air supply
Captured: 1st-order chamber dynamics
MECHANICAL - Vibration along aluminium frame
Captured: NO (rigid bases assumed)
Phase 2: modal analysis
THERMAL - Motor heat to ambient
20

## Slide 22
REAL-TIME EXPERIMENT ON THE ALIX LINE
The experimental sequence:
t (s) | Action | Station
0 | Pot enters the line from the input magazine | (upstream)
5 | XY10 vacuum gripper picks the empty pot from the input tray | XY10
7 | XY10 places the pot onto the moving conveyor belt | XY10 → Conveyor
8 → 18 | Conveyor transports the pot along the line (0.196 m/s steady state) | Conveyor
18 | Pot arrives at the CR5 capping station, photoelectric sensor S2 triggers | Conveyor
19 | CR5 picks a cap from the cap dispenser | CR5
22 | CR5 places the cap on the pot, vision check confirms placement | CR5
24 | Conveyor restarts and carries the capped pot downstream | Conveyor
30 | Cycle complete next pot enters | ---
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
21

## Slide 23
23

## Slide 24
PER-SUBSYSTEM VALIDATION RESULTS
CONVEYOR (against first.tdms, 150-250 s steady window)
Signal | R² | NRMSE | MAE | FIT % | Peak ratio
Voltage | 0.9987 | 0.0132 | 3.22 V | 96.34 | 1.002
Current(raw) | 0.5327 | 0.084 | 0.41 A | 32.10 | 0.83
Current(aligned) | 0.9124 | 0.029 | 0.13 A | 70.40 | 0.83
Temperature | 0.992 | 0.025 | 0.30 K | 91.18 | 0.992
XY10 (against four.tdms burst, 85-100 s)
Signal | Value
Position x | 0 to 0.250 m
Position y | 0 to 0.200 m
Position z | 0 to 0.050 m
Peak current i_x | 0.041 A
Peak current i_y | 0.042 A
Peak power | 6.65 W
Energy/cycle | 12.43 J (model) vs 4922 J (measured)
24

## Slide 25
PER-SUBSYSTEM RESULTS VALIDATION
CONVEYOR -Rs sweep [6, 8, 10, 12, 14, 16] ohm
I_rms model: 1.624 to 1.633 A (0.6 % variation)
I_rms measured: 1.144 A
CONCLUSION: Rs is NOT sensitive at this operating point
ROOT CAUSE: I_no_load ~ V_phase / (omega * L_m), Rs irrelevant
PHASE 2: Unlock L_m (currently 'fixed'), re-run optimiser
XY10 - friction sweep bx = by [5, 15, 25, 50, 100] N.s/m
Energy: 5.31 to 7.51 J (41 % sensitivity)
Measured: 4922 J (400x gap)
CONCLUSION: Friction tuning cannot close structural gap
ROOT CAUSE: DC-equivalent omits stepper holding current
PHASE 2: Add holding-current term, then calibrate friction
CR5 - joint damping d_J2 sweep [5, 10, 15, 20, 30]
Peak J2 omega: 14.5 to 3.9 rad/s (clear monotonic response)
Critical damping at d_J2 ~ 8
CONCLUSION: No measurement target available
PHASE 2: Instrument per-joint motor current

## Slide 26
VALIDATION
Two stages — against reality and against itself
STAGE A — FMU vs real TDMS field data
Does the model match the world?
Supply voltage conveyor current fundamental motor temperature rise XY10 burst envelope CR5 mass each compared against measurement.
STAGE B — FMU vs model
Did the export stay faithful?
The exported FMU is replayed in Python and compared to the original Dymola run catching any FMU-export bug. Result: essentially lossless (T_motor differs by 0.0001 K).
Signal-processing pipeline (Stage A)
1
Load TDMS
2
Apply ×200 / ×10 gains
3
200 ms steady window
4
Band-pass 40–60 Hz
5
FMU @ 50 kHz → decimate
6
Cross-correlation align
7
Compute 6 metrics
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
22

## Slide 27
STAGE A — FMU vs real TDMS field data
STAGE B — FMU vs model
25

## Slide 28
THE HEADLINE-PERFORMANCE METRICS
The model matches the line
0.999
Voltage R²
supply sinusoid · 99.8% peak
0.91
Current R²
fundamental, phase-aligned
99.2%
Thermal
ΔT 11.86 K vs 11.95 K obs.
94.9%
CR5 mass
23.74 kg vs 25 kg brochure
Supply voltage — TDMS measured (blue) vs model sinusoid (red)
R² = 0.9987 · peak 345.6 V vs 345.1 V (99.8%)
STAGE B — EXPORT IS LOSSLESS
T_motor
0.0001 K
> 99.99%
i_phase
0.00%
100%
P_elec
0.0003 W
> 99.99%
The FMU faithfully reproduces the Dymola model the toolchain itself introduces no error.
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
26

## Slide 29
SIX VALIDATION METRICS - what each one measures
R-squared R² =
Range: (-inf, 1]
Measures: variance explained by the model
(2) NRMSE (normalised root mean square error)
(3) MAE (mean absolute error)
(4) Peak ratio
PR =
27

## Slide 32
MODEL CALLIBRATION
5-STEP WORKFLOW
Cost function J(theta) = SUM (y_measured - y_model(theta))²
Design of experiments Train on first.tdms 150-250 s steady window Validate on second.tdms (cross-validation)
Sensitivity analysis S(y,theta_i) = (dy/dtheta_i) * (theta_i / y) Normalised so different parameters are comparable
Optimisation Levenberg-Marquardt via scipy.optimize.least_squares
Validation on held-out data
28

## Slide 33
30

## Slide 34
DELIVERABLES
10 delivered
Mechanical modelling
✓ Delivered
Electrical modelling
✓ Delivered
Thermal modelling
✓ Delivered
FMU export
✓ Delivered
Python orchestration
✓ Delivered
Validation vs measurements
✓ Delivered
10 are fully delivered. The two open items sensitivity/observability and parameter identification have their workflow and tooling (Dymola 2026x calibration UI) defined for Phase 2.
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
32
Model Calibration
✓ Delivered
Performance metrics
✓ Delivered
Energy Analysis
✓ Delivered
Discrete event scheduling
✓ Delivered

## Slide 35
CONCLUSION
A validated multiphysics digital model of the ALIX line — three subsystems, three physics domains — matching the real line to R² = 0.999 on voltage, 0.91 on current and 99.2% on thermal, with every residual physically explained.
1
Digital Twin Successfully Established
A complete multiphysics digital representation of the ALIX Industry 5.0 production line was successfully developed.
Three major subsystems (Conveyor, CR5, XY10) were modelled and exported as FMI-compliant FMUs.
End-to-end production-line orchestration was achieved through Python.
2
Experimental Validation Confirms Model Reliability
The developed models demonstrated strong agreement with real industrial measurements, validating their suitability for engineering analysis and decision support.
Voltage prediction accuracy: R² = 0.999
Current prediction accuracy: R² = 0.91
Thermal prediction accuracy: 99.2%
3
Foundation for Industry 5.0 Optimization
Beyond simulation, the digital twin enables future predictive maintenance, energy optimization, and intelligent production-line reconfiguration.
Model architecture supports parameter identification, sensitivity analysis, and real-time monitoring.
Samiksha Satre · Euler Laboratory, ISAE-Supméca · github.com/samikshasatre/Mechatronics-modelling-of-entire-industry-5.0
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
33

## Slide 36
THANK YOU OPPORTUNITY😊
"From a tier-two city in Maharashtra to a research laboratory in Paris — this internship is the longest distance I have ever travelled, in every sense of the word. Thank you for making it possible."
1
TECHNICAL SKILLS
2
INTERPERSONAL & METHODOLOGICAL
3
Foundation for Industry 5.0 Optimization
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
26
Dymola on 3DEXPERIENCE
FMI 2.0 co-simulation
GIT/GITHUB
Nptdms
Anaconda
Modelica
Multiphysics coupling
Signal processing
CAD-to-model workflow
Engineering rigour
Scope discipline
Working in a research lab
Cross-cultural collaboration
Honest scientific communication
Translating supervisor feedback into structured work
Four months in Paris
Daily life at ISAE-Supméca and the Euler Lab
Discovering French engineering culture
First international internship
A perspective I will keep my whole career
21

## Slide 37
THANKING ALL 😊
Project Guides Name
Mr. Romain Delabeye
Mr. Roshan Pushan
Dr. Shriniwas Metan
Mr. Moncef HAMMADI
Mr. Thierno DIALLO
La Fondation Dassault System France
Mr. Heman Gadgil
Mr. Salim Huzefa
Ms. Marie Pierre AULAS
Mr. GALEA Jean-Marc
1
ALIX · Industry 5.0 Digital Twin | Euler Laboratory, ISAE-Supméca
26
NKOCTE & ISAE SUPMECA INSTITUTE
Mr. Sudhirkumar Dhotre
Mr. Adarsh Chandanshive
Dr. P .D .Bahirgonde
Mr. R. R. Patil
Mr. Akhtar Nadaf
Dr. Francesco Ciampi
22